Chapter 14, Problem 1.

Find the transfer function Vo/Vi for the following circuit.

Solution

where 0 = 1/RC

This is a high pass filter (HPF).

The 3 dB point is at  = 0

Chapter 14, Problem 3

(a)  For the circuit below, determine the transfer function H(s) = Vo(s)/Vi(s)

(b)  If R = 40 k and C = 2 F, specify the locations of the poles and zeros of H(s)

Solution

(a)  The Thevenin Impedance at the terminals of the right hand capacitor is

Zt = R + R║1/sC = R + R/(1 + sRC)

Then from the simple Thevenin circuit,

(b)	RC = 40 x 103 x 2 x 10-6 = 0.08

There are no zeros and the poles are at

s1 = -0.383/RC = -4.787

s2 = -2.617/RC = -32.712

Chapter 14, Problem 5.

Find the transfer function H() = Vo/Vi for these circuits

Solution

(a)	This is simply a voltage divider network

(b)	R║1/jC = R/(1 + jRC)

Then voltage divider gives

Chapter 14, Problem 6

Find the transfer function H() = Io/Is in the following circuits.

Solution

(a)	Using current division

(b)	Apply NVA to the circuit

The last term is Io, giving

V = 2Io(jL + 1/jC)

This allows us to eliminate V

by multiplying these two equations together

Chapter 14, Problem 7.

Calculate |H()| if HdB equals

(a)		0.05 dB

(b)		-6.2 dB

(c)		104.7 dB

Solution

(a)		0.05 = 20 log10H

log10H = 0.0025

H = 1.00577

(b)		20 log10H = -6.2

log10H = -0.31

H = 0.4898

(c)		20 log10H = 104.7

log10H = 5.235

H = 1.718 x 105

Chapter 14, Problem 8.

Determine the magnitude in dB and the phase in degrees of H() at  = 1 if H() equals

(a)		0.05

(b)		125

(c)		10j/(2 + j)

(d)		3/(1 + j) + 6/(2 + j)

Solution

(a)	HdB = 20 log100.05 = -26.02		 = 0º

(b)	HdB = 20 log10125 = 41.94		 = 0º

(c)	H(1) = j10/(2 + j) = 4.472 < 63.43º

HdB = 20 log104.472 = 13.01,	 = 63.43º

(d)	H(1) = 3/(1+j) + 6/(2+j) = 3.9 – j1.7

= 4.254 <-23.55º

HdB = 20 log104.254 = 12.577		 = -23.55º

Chapter 14, Problem 9.

A ladder network has a voltage gain of

Sketch the Asymptotic Bode plot for the gain (amplitude only)

Solution

low frequency asymptote (lfa) is

H = 1 or HdB = 0 dB

Poles at  = 1 and  = 10

Chapter 14, Problem 11.

Sketch the amplitude ABP for

Solution

We can re-write the transfer function

The lfa is H() = 5/j

When  = 1, its value is 5, or 14 dB

Its slope is -20 dB/decade

There is a pole at  = 2, and a zero at  = 10

Chapter 14, Problem 15.

Construct the magnitude ABP for

s = j

Solution

lfa is 2 → 6 dB

Zero (up) at  = 1

Poles (down) at  = 2 and 10

Chapter 14, Problem 17.

Draw the magnitude ABP for

Solution

lfa is	0.25 s

This has a dB value of 20 log(0.25) = -12 dB, at  = 1, and a slope of +20 dB/decade.

There is one pole at  = 1 and there are two poles at  = 2. The slope changes from +20 to zero at  = 1 and it changes from zero to -40 at  = 2.

Chapter 14, Problem 18.

Draw the magnitude ABP for

Solution

lfa is 4/(50s)

This has a slope of -20 dB/decade, and passes through  = 1 with a value of 20 log(4/50) = -22 dB.

There are two zeros (up) at  = 2

There are two poles (down) at  = 5 and  = 10

The slope will change from -20 to +20 at  = 2, to zero at  = 5, and to -20 at  = 10

Chapter 14, Problem 22.

Find the transfer function with the magnitude ABP shown below.

Solution

lfa is 20 dB, equivalent to a lf gain of k where 20 log K = 20, that is, k = 10

There is a zero at  = 2, and poles at  = 20 and  = 100. Therefore the transfer function is

This could be re-written as

s = j

# Text boxes

vi(t)

C

R

R				R

Vi	       C			       C

+

Vo

-

+

Vi

-

+

Vo

-

R		L

C

(a)

(b)

C

R

+

Vo

-

+

Vi

-

L

is		     20 			0.25 F

10 H

io

(a)

(b)

io

0.1 F

is		     10 			2.5 H

0.5 v

+

v

-

0.1		1		10		100		1000

0

-20

-40

-60

-80

-40 dB/decade

-20 dB/decade

-20 dB/decade

14 dB

20

0

-20

-40

-60

0.1		1		10		100		1000

6 dB

-20 dB/decade

20

0

-20

-40

-60

0.1		1		10		100		1000

-12 dB

-40 dB/decade

20

0

-20

-40

-60

0.1		1		10		100		1000

20 dB/decade

-20 dB/decade

-22 dB

20 dB/decade

20

0

-20

-40

-60

0.1		1		10		100		1000

2		20		100

H(dB)

40

20

0

-20 dB/decade