Chapter 3, Problem 1.

Determine v1, v2 and the power dissipated in all the resistors in this circuit.

Solution:

KCL at node 1

6 = v1/8 + (v1- v2)/4	→	48 = 3 v1 – 2 v2

KCL at node 2

(v1 – v2)/4 = v2/2 + 10	→	40 = v1 – 3 v2

Solving these two equations gives

v1 = 9.143 V,		v2 = -10.286 V

P8 = v12/8 = 9.1432/8 = 10.45 W

P4 = (v1 – v2)2/4 = 94.37 W

P2 = v22/2 = 10.2862/2 = 52.9 W

Chapter 3, Problem 5.

Find vo in this circuit

Solution:

Apply KCL to the top node

(30 – vo)/2 k + (20 – vo)/5 k = vo/4 k

So vo = 20 V

Chapter 3, Problem 6.

Use nodal analysis to obtain vo in this circuit.

Solution:

i1 + i2 + i3 = 0			that is;

(vo – 12)/4 + vo/6 + (vo – 10)/2 = 0

giving vo = 8.727 V

Chapter 3, Problem 10.

Find io in this circuit

Solution:

Nominate node voltages, v0, v1 and v

At node 1, we have

(v2 – v1)/1 = 4 + v1/8

At node 0, we have

4 = v0/2 + 2 i0 and i0 = v1/8

giving		16 = 2 v0 + v1

At node 2 we have

2 i0 = (v2 – v1)/1 + v2/4	and		i0 = v1/8

giving		v2 = v1

The solution is

v0 = 24 V, v1 = v2 = -32 V, i0 = - 4 A

Chapter 3, Problem 12.

Use nodal analysis to find currents i1 and i2 in this circuit.

Solution

Name v1, v2 as the voltages at the two upper nodes

At node 1,	(24 – v1)/10 = (v1 – v2)/20 + v1/40

ie		96 = 7 v1 – 2 v2

At node 2,	5 + (v1 – v2)/20 = v2/50

ie		500 = -5 v1 + 7 v2

Solving these two equations gives

v1 = 42.87 V and v2 = 102.05 V

Therefore

i1 = v1/40 = 1.072 A

i2 = v2/50 = 2.041 A

Chapter 3, Problem 16.

Find v1, v2 and v3, using NVA

Solution

The resistances are given as conductances, in Siemens. The dotted line contains a supernode which gives

2 = v1 + 2(v1 – v3) + 8(v2 – v3) + 4v2

ie		2 = 3v1 + 12v2 – 10v3

But		v1 = v2 + 2v0 and v0 = v2

So		v1 = 3v2

v3 = 13 V

Solving these equations, we have

v1 = 18.858 V

v2 = 6.286 V

v3 = 13 V

Chapter 3, Problem 17.

Using nodal analysis, find current i0

Solution

We need KCL at nodes 1 and 2

(60 – v1)/4 = v1/8 + (v1 – v2)/2

ie		120 = 7 v1 – 4 v2			(1)

3 i0 + (60 – v2)/10 + (v1 – v2)/2 = 0

But		i0 = (60 – v1)/4

So

3x(60 – v1)/4 + (60 – v2)/10 + (v1 – v2)/2 = 0

ie 1020 = 5 v1 – 12 v2			(2)

Solving (1) and (2) gives

v1 = 53.08 V

Hence i0 = (60 – v1)/4 = 1.73 A

Chapter 4, Problem 8

Apply superposition to find i in this circuit.

Solution

Let i = i1 + i2, where i1 and i2 are due to current and voltage sources respectively.

If 20 V is a S/C, we have a current divider circuit with two resistors

i1 = 6/(6 + 4) x 5 = 3 A

If 5 A source is O/C, we have a single loop

i2 = 20/(6 + 4) = 2 A

This i = i1 + i2 = 3 + 2 = 5 A

Chapter 4, Problem 10

Find the terminal voltage, Vab, using superposition

Let Vab = v1 + v2 where v1 and v2 are due to the 4 V and the 2 A sources respectively

If the 2 A source is set O/C, then no current flows in the resistor. The terminal voltage is v1. Applying KVL, we have

-v1 – 3v1 + 4 = 0

ie		v1 = 1 V

If the 4 V source is S/C, we have a loop carrying 2 A. We apply KVL

- v2 – 3 v2 + 10 x 2 = 0

ie		v2 = 5 V

So		Vab = v1 + v2 = 1 + 5 = 6 V

# Text boxes

6A		   8			2		10A

v1	4		v2

+

-

30 V

2 k

20 V

5 k

+

-

4 k

+

vo

-

+

-

+      -

4		        vo    10V

i1				i2				      i3

12 V		  6				       2

1 

4 A					2 io

8 		        2 				    4 

io

v1			      v0				  v2

+

-

10 		v1	20 		v2	30 

24 V		    40 		      5 A  20 

i1				     i2

+    -

+

-

2 S

v1	   2v0		      v2	     8 S	v3

2A	     1S	    4 S		  13 V

+

v0

-

i0

4 					2 

10 

60 V

3 i0

8 

+

-

v1

v2

6 

4 

+

-

20 V

5 A

i

+

-

4 V			      2 A			  Vab

+

+     -

10 		3 Vab

a

b