Chapter 4, Problem 20

Use source transformation to find i in this circuit

Solution

Transform the voltage source an 6  resistor to give the following circuit

We can now combine the two current sources, since they are in parallel, and we can combine the 6  and 3  resistors

From this circuit, we have  i = 6/2 = 3 A

Chapter 4, Problem 27

Apply source transformation to find vx in this circuit

Solution

Transform the voltage sources to give the following circuit

We can now convert the left hand part of the circuit to a Thevenin equivalent and the right hand part of the circuit to another Thevenin equivalent.

10║40 = 8 ohms

The current around this loop is

i = (40 – 200)/40 = - 4 A

So vx = 12 x -4 = - 48 V

Chapter 4, Problem 34

Find the Thevenin equivalent of this circuit at the terminals a-b

Solution

We find VOC using node voltage analysis.

At node 1

(40 – v1)/10 = 3 + (v1 – v2)/20 + v1/40

ie		40 = 7 v1 – 2 v2

At node 2

3 + (v1 – v2)/20 = 0

ie

Since there are no dependent sources in this circuit, we can calculate Rt simply by setting the independent sources to zero. The result is as follows

So Rt = 20 + 10║40 = 20 + 400/50 = 28 

Chapter 4, Problem 48

Determine the Norton equivalent of this circuit at terminals a-b.

To find the O/C voltage, we note that i0 = 2 A.

Then the dependent source is 10 i0 = 20 V.

So Vt = 4 x 2 – 20 = - 12 V

When the terminals a-b are S/C, we have KCL

2 = v/4 + (v – 10 i0)/2

and		i0 = v/4

We solve for v to get	v = - 4 V

Then IN = ISC = 2 - i0 = 2 – v/4 = 2 + 1 = 3 A

RN = Vt/IN = - 12/3 = - 4 

Note the possibility of a circuit with active components (dependent source) having negative resistance.

Chapter 4, Problem 71

What resistor, connected across terminals a-b will absorb maximum power from this circuit? What is that power?

Solution

We need the Thevenin equivalent circuit at terminals a-b.

v0 = 8 x 1/(1 + 3) = 2 V

Dependent source is -120 x 2 = -240 V

Vt = VOC at a-b is -240 x 40/(40 + 10) = -192 V

ISC at a-b is -240/10k = -24 mA

So Rt is -192/(-24m) = 8 k

For maximum load power, load resistance is 8 k.

Then load current is 192/16k = 12 mA

Power is (12*10-3)2 x 8*103 = 1.152 W

Chapter 4, Problem 75

Determine the value of R in this circuit so that the maximum power which can be delivered to the load is 3 mW

Solution

Since there are no dependent sources, we can set all sources to zero and find Rt as the parallel combination of all three resistances, R.

Rt = R/3

We can find VOC by using KCL at the output.

(1 – VOC)/R + (2 – VOC)/R + (3 – VOC)/R = 0

Vt = VOC = 2

For maximum power transfer, RL = Rt = R/3

Pmax = Vt2/4Rt = 1/Rt = 3 mW

Rt = 1000/3

So R = 3 Rt = 1000 

Chapter 5, Problem 2.

The open-loop gain of an OpAmp  is 100,000. Calculate the output voltage when there are inputs of + 10 v on the inverting terminal and + 20 V on the noninverting terminal.

Solution

vo = Avi = A (v2 – v1)

= 105 (20 – 10) * 10-6

= 1 V

# Text boxes

+

-

6 

12 V	    2 		   3 	      4 A

i

i

2 A  6 	      2 		      3 	          4 A

2 		           2 	               6 A

i

+

-

+

-

10 			12 			20 

+  vx  -

50 V	     40 		8 A		    40 V

5 A	   10 40 		  8 A		  20 2 A

+  vx  -

12 

+  vx  -

40 V	   		  		  		200 V

8 			12 			20 

+

-

+

-

+

-

40 V

10 				20 

40 

3 A

a

b

a

b

v1

40 

10 				20 

+     -

v2

2 A

4 

2 

10 i0

i0

a

b

v

+    -

-

+

3 k					10 k

8 V	v0	1 k			  120 v0	     40 k

a

b

+

-

R

R

R

+

-

+

-

+

-

1 V

2 V

3 V

RL